## Slide 1
FIELD GUIDE / VERSION 3
Motor test patterns
Usage, motion meaning and result interpretation
motor_control_g4dual / TEST PATTERNS v3
01
One node. Five patterns.
A repeatable way to inspect
motor and platform behavior.
Straight / Rotate / Circle / Square / S
Commands: aic mc tp <pattern>
Editable guide + printable reference
Ideal S reference - not test data

## Slide 2
01 / PATTERN MAP
Choose the question before the pattern
All commands execute inside the existing motor_control_node.
motor_control_g4dual / TEST PATTERNS v3
02
straight
Forward + reverse
Wheel balance; reverse response
rotate
Left + right in place
Turn symmetry; angle repeatability
circle
Constant-radius lap
Wheel-speed ratio; radial drift
square
4 lines + 4 stopped turns
Distance/angle error accumulation
s
Smooth left/right bend
Transition response; path correction
Default repetitions: 3 pairs for straight/rotate; 3 complete shapes for circle/square/S.

## Slide 3
02 / OPERATING SEQUENCE
Start a test from standstill
Build/install the updated node and deploy the updated AICamera helper on the robot.
motor_control_g4dual / TEST PATTERNS v3
03
ros2 run motor_control_g4dual motor_control_node \
--ros-args --params-file /path/to/motor_control.yaml \
-p enable_can:=true
One shell command; replace the parameter-file path.
1 Stop periodic cmd_vel publishers.
2 aic mc en -> aic mc e diag
3 Wait for fresh feedback + standstill.
4 aic mc tp straight
Monitor in another terminal
aic mc tp status
Required before starting
CAN on; motors enabled; no fault latch.
Previous command must expire
Default cmd_vel timeout: 500 ms.
RPM resolution: 1.0 RPM/unit.
Confirmed for this project.
YAML, launch and CLI agree.
Other projects are unchanged.

## Slide 4
03 / STRAIGHT
Straight: compare forward and reverse
One repetition = forward 1 m, stop, reverse 1 m, stop.
motor_control_g4dual / TEST PATTERNS v3
04
aic mc tp straight
FORWARD 1 m
REVERSE 1 m
Same physical line; paths offset here for clarity.
Amber dots indicate a standstill check.
What it tells you
Left/right wheel balance and reverse response.
Default motion
0.1 m/s; 3 forward/reverse pairs.
How it finishes
Distance projected onto each segment heading.
Interpretation
Return error is measured, not corrected.

## Slide 5
04 / ROTATE
Rotate: isolate turning behavior
One repetition = left 90 degrees, stop, right 90 degrees, stop.
motor_control_g4dual / TEST PATTERNS v3
05
aic mc tp rotate
LEFT 90 deg / RIGHT 90 deg
What it tells you
Turning symmetry and repeatable angles.
Default motion
0.2 rad/s; 3 left/right pairs.
Configurable angle
angle_deg supports 90, 180 or 360 degrees.
How it finishes
Continuous yaw handles the +/-180 boundary.

## Slide 6
05 / CIRCLE
Circle: compare inner and outer wheels
One repetition = one full lap, then standstill. Default: counterclockwise.
motor_control_g4dual / TEST PATTERNS v3
06
aic mc tp circle
R = 1 m
Robot-centre radius; wheel paths differ.
What it tells you
Wheel-speed ratio and radius consistency.
Default motion
Radius 1 m; 3 laps; about 64 s per lap.
Motion relationship
v = radius x angular speed; limits apply.
How it finishes
Accumulated yaw reaches 360 deg, then stop.

## Slide 7
06 / SQUARE
Square: expose accumulated error
One repetition = four forward sides and four stationary 90-degree turns.
motor_control_g4dual / TEST PATTERNS v3
07
aic mc tp square
1 m / side
8 segments
Stop after every line and turn; schematic only.
What it tells you
Distance, turn and stop errors accumulate.
Default motion
1 m sides; counterclockwise; 3 squares.
Fixed corners
Always 90 deg; angle_deg only affects rotate.
How it finishes
Includes the last turn toward the start heading.

## Slide 8
07 / S CURVE
Smooth S: test transition and correction
One repetition = a continuous left/right bend; stop only at the end.
motor_control_g4dual / TEST PATTERNS v3
08
aic mc tp s
NO STOP AT THE MIDDLE
Ideal reference; end is displaced from start.
What it tells you
Smooth turning response and tracking error.
Default geometry
4 m travel length; 1 m minimum nominal radius.
Path correction
Heading + lateral gains default to 1.0.
For motor-only response
Set both S gains to 0, then restart the node.

## Slide 9
08 / PARAMETERS
Change geometry, limits and direction
Edit motion_test.* in motor_control.yaml, then restart the node.
motor_control_g4dual / TEST PATTERNS v3
09
Parameter suffix
Default
Meaning
distance_m / angle_deg
1.0 / 90.0
Straight segment / rotate angle
circle_radius_m / square_side_m
1.0 / 1.0
Circle radius / square side
s_length_m / s_radius_m
4.0 / 1.0
S travel length / minimum nominal radius
clockwise
false
Circle/square clockwise; S right-first if true
linear_speed_mps / angular_speed_radps
0.1 / 0.2
Body velocity limits
linear_accel_mps2 / angular_accel_radps2
0.1 / 0.2
Body acceleration limits
s_heading_gain / s_lateral_gain
1.0 / 1.0
S correction: 1/s and 1/m^2
repetitions
3
Pairs or complete shapes, depending on pattern
The feature defaults to enabled. It does not start tests or enable motors automatically.

## Slide 10
09 / COMMAND OWNERSHIP
Normal commands can take over
Tests and normal driving share the same node and motor enable state.
motor_control_g4dual / TEST PATTERNS v3
10
TEST RUNNING
cmd_vel
NORMAL DRIVE
Valid cmd_vel, including zero
Ends the test and takes control with that command.
Normal completion
Zero speed; motors stay enabled for the next command.
Cancel, fault or emergency stop
Motion is gated; explicitly re-enable after resolving it.
Pause periodic cmd_vel publishers while testing, or their next message will interrupt the test.

## Slide 11
10 / CSV & MEANING
Read the result, not only the status
aic mc tp status shows state, segment, outcome reason and the CSV path.
motor_control_g4dual / TEST PATTERNS v3
11
ILLUSTRATIVE STOPPED RESULT
Target 1.000 m
Measured 1.025 m
Difference +0.025 m
+25 mm overshoot
last_stopped_segment_progress
- last_stopped_segment_target
Check units and segment type
line / s_curve: m turn / arc: rad
Compare targets and feedback
Normalized wheel RPM; account for feedback delay.
Inspect path_error_m
Lateral / radial / turn translation / S cross-track.
CSV directory on the robot
/tmp/motor_control_tests (configurable)
completed = sequence finished. Wheel odometry is not independent proof of ground-track accuracy.

## Slide 12
11 / TROUBLESHOOTING
If a test will not start or stops early
A published command is a request. Check status for acceptance or the reason for interruption.
motor_control_g4dual / TEST PATTERNS v3
12
Rejected before start
Check enabled motors, CAN, fresh position + speed feedback.
Recent cmd_vel / moving wheels
Stop command publishers; wait for timeout and standstill.
Aborted: external cmd_vel
Normal command took control; the test will not resume.
No progress / stale feedback
Inspect obstruction, wheel direction, encoders and CAN.
Segment timeout
60 s per movement/wait; circle motion has a 120 s default.
CSV cannot be written
Use a writable local log directory; check disk space.
Feedback timeout: 500 ms. Stall timeout: 5 s. Standstill: both wheels <= 0.5 RPM for 0.5 s.
Cancel requests the existing ramp stop; an aborted state does not confirm physical standstill.

## Slide 13
12 / QUICK REFERENCE
Commands to keep beside the robot
Use one pattern at a time. Begin with short, low-speed runs and inspect the record.
motor_control_g4dual / TEST PATTERNS v3
13
aic mc tp straight
Forward / reverse
aic mc tp rotate
Left / right rotation
aic mc tp circle
Full circle
aic mc tp square
Stopped-corner square
aic mc tp s
Smooth S
aic mc tp status
Monitor outcome + CSV
aic mc tp cancel
Cancel and gate motion
aic mc tp help
Show command help
Observe -> compare -> tune -> repeat. Validate physical accuracy using external measurements.